## Slide 1: I/O Voltage Question why am I reading less then 5 volts on the output I/O pin
Atmega 328P Data sheet
? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ? ?

## Slide 2: Atmel I/O circuit schematic
Voltage source resistor
+ 5 volts
FET switch
I/O pin
pulled up mode

## Slide 5: Programming “Arduino”
LCD Displays
Interfaces & Sketches
Instructor / Facilitator - Alan Rux

## Slide 6: Liquid Crystal Displays

## Slide 7: Liquid Crystal Displays
a optical twisted light nematic device
All the LCD displays controller IC’s use the architecture introduced by Hitachi
Most of the LCD Displays available in the market are 16X2 (That means, the LCD displays are capable of displaying 2 lines each having 16 Characters a line)

## Slide 8: Character vs. Graphical LCDs
Pixel size from 100 X 100
to
1000 X 750 pixels
Display graphical
images
5 X 7 pixel rectangles
rolls & columns
Display text

## Slide 9: 2X16 Display Front and Back View

## Slide 10: LCD Block Diagram

## Slide 11: Liquid Crystal Displays Characters
5 by 7 or 5 by 8 pixels

## Slide 12: Liquid Crystal Displays Pixels
Bit 7 is MSB

## Slide 13: Viewing Angle of LCDs
Typical +/- 30 degrees, General Liquid Crystal Displays have a limited viewing angle. They lose contrast and become hard to read at some viewing angles

## Slide 14: Displays come in colors and with or without back-lighting

## Slide 15: LCD Pin Configuration 16 X 2 display

## Slide 16: LCD back-light schematic 16 X 2 display
10 K pot.

## Slide 17: Connecting to Arduino
The Hitachi-compatible LCDs can be controlled in two modes: 4-bit or 8-bit. The 4-bit mode requires seven I/O pins from the Arduino, while the 8-bit mode requires 11 pins. For displaying text on the screen, you can do most everything in 4-bit mode.
To wire your LCD screen to your Arduino, connect the following pins:
LCD RS pin to digital pin 12
LCD Enable pin to digital pin 11
LCD D4 pin to digital pin 5
LCD D5 pin to digital pin 4
LCD D6 pin to digital pin 3
LCD D7 pin to digital pin 2
Additionally, wire a 10K pot to +5V and GND, with it's wiper (output) to LCD screens VO pin (pin3).

## Slide 18: Connecting to Arduino

## Slide 19: Connecting to Arduino
4 Bit Data Mode
Contrast adjust control 10K ohms pot
Wire pin 15 to +5 v with 220 ohms resistor in series,
pin 16 to gnd.

## Slide 20: LCD Sketch “Hello, SVECW” +second count p.1
* LCD RS pin to digital pin 12 * LCD Enable pin to digital pin 11 * LCD D4 pin to digital pin 5 * LCD D5 pin to digital pin 4 * LCD D6 pin to digital pin 3 * LCD D7 pin to digital pin 2 * LCD R/W pin to ground * 10K resistor: * ends to +5V and ground * wiper to LCD VO pin (pin 3) */

## Slide 21: LCD Sketch “Hello, SVECW” +second count p.2
// include the library code: #include <LiquidCrystal.h> // initialize the library with the numbers of the interface pins LiquidCrystal lcd(12, 11, 5, 4, 3, 2); void setup() { // set up the LCD's number of columns and rows: lcd.begin(16, 2); // Print a message to the LCD. lcd.print(“Hello, SVECW"); } void loop() { // set the cursor to column 0, line 1 // (note: line 1 is the second row, since counting begins with 0): lcd.setCursor(0, 1); // print the number of seconds since reset: lcd.print(millis()/1000); }

## Slide 22: References LiquidCrystal
#include <LiquidCrystal.h> #include is used to include outside libraries in your sketch. <LiquidCrystal.h> is the library based on the Hitachi HD44780
LiquidCrystal lcd(12, 11, 5, 4, 3, 2);
LiquidCrystal(rs, enable, d4, d5, d6, d7)
rs: the number of the Arduino pin that is connected to the RS pin on the LCD
enable: the number of the Arduino pin that is connected to the enable pin on the LCD
d0, d1, d2, d3, d4, d5, d6, d7: the numbers of the Arduino pins that are connected to the corresponding data pins on the LCD.
d0, d1, d2, and d3 are optional;
if omitted, the LCD will be controlled using only the four data lines
d4, d5, d6, d7

## Slide 23: References LiquidCrystal p2
begin() Initializes the interface to the LCD screen, and specifies the dimensions (width and height) of the display. begin() needs to be called before any other LCD library commands
lcd.begin(cols, rows);
lcd: a variable of type LiquidCrystal
cols: the number of columns that the display has
rows: the number of rows that the display has
lcd.begin(16, 2);
# of columns , # of rows

## Slide 24: References LiquidCrystal
setCursor() setCursor() method to reposition the cursor. To move the cursor, just call setCursor() with a row and column position.
lcd.setCursor(0, 1);
column #, row #
( 0,0)
2x16 display (column#, row#)
( 15,0)
( 0,1)
( 15,1)

## Slide 25: References LiquidCrystal p3
lcd.print(millis()/1000);
millis() Returns the number of milliseconds since the Arduino board began running the current program.
/1000 divides the number of milliseconds by 1000 to get seconds

## Slide 26: Arduino Digital Voltmeter
A 10k pot was added to solderless breadboard, pot ends connected to +5v & gnd., pot. center arm to analog input pin A0

## Slide 27: Digital Voltmeter
0 to 5v. Trimpot with wiper arm to analog input pin A0
0 to 5v. Trimpot with wiper arm to LCD contrast adjust pin VE

## Slide 28: Digital Voltmeter Connections to Arduino & LCD
0 to 5volts
Input to A/D pin A0
220 ohms
Resistor for IC pin
protection

## Slide 29: Arduino Digital Voltmeter Sketch p1
/*
LCD RS pin to digital pin 12 LCD Enable pin to digital pin 11 LCD D4 pin to digital pin 5 LCD D5 pin to digital pin 4 LCD D6 pin to digital pin 3 LCD D7 pin to digital pin 2 LCD R/W pin to ground pot wiper to LCD VO pin (pin 3) Potentiometer attached to analog input 0 center pin of the pot. to the analog pin A0 */
#include <LiquidCrystal.h> //include the library code.
int val = 0;
LiquidCrystal lcd(12, 11, 5, 4, 3, 2); // LCD pins connected to the arduino pins

## Slide 30: Arduino analog input display Sketch p2
void setup() {
// set up the LCD's number of columns and rows.
lcd.begin(16, 2); //initializes interface to LCD screen
pinMode(A0, INPUT);
lcd.setCursor(0,0); //sets LCD start point, Col 0, Row 0 for next line of code
lcd.print("0-5v. METER"); // display of 1st line on LCD
lcd.setCursor(0,1); //sets LCD start point, Col 0, Row 1 for next line of code
lcd.print("Volts="); // display 2nd line on LCD
}

## Slide 31: Arduino analog input display Sketch p3
void loop() {
lcd.setCursor(7,1); //sets LCD start point, Col 7, Row 1 for voltage value
lcd.print(analogRead(0)/204.6); //Converts arduino's 0-1023 to 0.00-5.00
delay(300); //delay of 3ooms. for stability
}

## Slide 32: Digital Light meter DYIASDE
Using the light-dependent resistors from the A/D converter input slide sets design me a “Light Meter” and display the reading in “LUX” values.
I used a 10K ohm resistor and had a voltage swing of 4.7v to .45v, bright light to dark. Some <,> math functions might be needed for ruff calibration.
A step function is OK for this Lab., at least 6 steps please.
Enjoy your Lab.
LDR

## Slide 33: Digital Light meter DYI
10k resistor
Light Dependent Resistor